# CE543: Introduction to Geotechnical Earthquake Engineering
# Homework Assignment #5

March 10th, 2026

To: Dr. Arash Khosravifar
From: Brandon Auyeung
## Problem 1.
A series of undrained cyclic simple shear tests were performed on Ko-consolidated specimens of saturated sand at a relative density of 50%. The cyclic loading consisted of uniform sinusoidal shear loads. Tests were performed at three different initial vertical effective consolidation stresses, with the results tabulated below.
### Find:
#### Part A
Estimate the cyclic shear stress that would be required to trigger ru=100% in 15 uniform undrained loading cycles for a specimen of this sand having an initial vertical consolidation stress of 450 kPa.
#### Part B
For the cyclic resistance ratio (CRR) defined as the cyclic stress ratio that triggers ru=100% in 15 uniform cycles of loading, determine the value of Kσ for an effective consolidation stress of 450 kPa.
### Solution:
#### Part A
The CSR can be obtained by dividing the τcyc value by the effective consolidation stress that is used to consolidate the sample.
\begin{tabular}{*{4}{c}} Test & CSR, \sigma_{3c}' = 40 \ \text{kPa} & CSR, \sigma_{3c}' = 160 \ \text{kPa} & CSR, \sigma_{3c}' = 600 \ \text{kPa} \\ \hline \hline a & 0.272500 & 0.261250 & 0.167833 \\ \hline b & 0.180000 & 0.163750 & 0.118333 \\ \hline c & 0.142500 & 0.125000 & 0.113500 \\ \hline d & 0.120000 & 0.104375 & 0.068333 \\ \hline \end{tabular}

Table 1. Values of CSR per test letter.
The values of CSR can be fit to a power fit with the number of cycles to failure (i.e. N to failure) as the independent values (i.e. CSR = αNβ).

Figure 1. CSR plotted with respect to N to failure, along with power fit model on different effective consolidation stresses.
The CSR at N = 15 for σ3c’ = 450 kPa is between the power fits of CSR at N = 15 for σ3c’ = 160 kPa and CSR at N = 15 for σ3c’ = 600 kPa. Linear interpolation can be used to determine the value of CSR at N = 15 for σ3c’ = 450 kPa and thus the value of τcyc at N = 15 for σ3c’ = 450 kPa.
\frac{CSR_{600}(N = 15) - CSR_{160}(N = 15)}{\Delta \sigma_{3c}'} = \frac{CSR_{450}(N = 15) - CSR_{160}(N = 15)}{\Delta \sigma_{3c}'}

\frac{0.1347- 0.1152}{600 \ \text{kPa} - 160 \ \text{kPa}} = \frac{CSR_{450}(N = 15) - 0.1152}{450 \ \text{kPa} - 160 \ \text{kPa}}	Linear Interpolation

CSR_{450}(N = 15) = 0.1219

CSR_{450}(N = 15) = \frac{\tau_{cyc}}{\sigma_{3c}'} \Rightarrow \tau_{cyc} = \sigma_{3c}' CSR_{450}(N = 15) = 0.1219(450 \ \text{kPa}})

\tau_{cyc} = 54.8 \ \text{kPa}

#### Part B
The value of Kσ requires the CRR at 1 atm (i.e. 100 kPa). This value can be found via linear interpolation between the power fits.
\frac{CSR_{160}(N = 15) - CSR_{40}(N = 15)}{\Delta \sigma_{3c}'} = \frac{CSR_{100}(N = 15) - CSR_{40}(N = 15)}{\Delta \sigma_{3c}'}

\frac{0.1152 - 0.1506}{160 \ \text{kPa} - 40 \ \text{kPa}} = \frac{CSR_{100}(N = 15) - 0.1506}{100 \ \text{kPa} - 40 \ \text{kPa}}	Linear Interpolation

CSR_{100}(N = 15) = 0.1427

K_\sigma(\sigma_{3c}' = 450 \ \text{kPa}) = \frac{CSR_{450}}{CSR_{100}} = \frac{0.1219}{0.1427}

K_\sigma = 0.854

## Problem 2.
### Given:
The soil profile at a level site consists of a 3-m thick layer of sandy clay, overlaying an 8-m thick layer of loose sand, overlaying stiff gravelly clays that extend to depths greater than 20 m. The water table is at a depth of 2 m and the ground water is initially hydrostatic. The total unit weight of the upper sandy clay, above or below the water table, is 18 kN/m3. The total unit weight of the loose sand layer is 20 kN/m3. The coefficient of lateral earth pressure at rest (Ko) in the loose sand is estimated to be 0.5. Two open standpipe piezometers were installed that had small enough slotted intervals that they provide essentially point measurements of ground water conditions: Piezometer A has its slotted interval at a depth of about 4 m, while Piezometer B has its slotted interval at a depth of about 10m.
### Find:
#### Part A
For the initial conditions, determine: (i) where the water levels (relative to the ground surface) would be in both piezometers, and (ii) the average hydraulic gradient between the slotted intervals of the two piezometers.
#### Part B
For the initial conditions, determine the total horizontal stress at the depth of the slotted interval for Piezometer B.
#### Part C
Suppose an earthquake causes liquefaction (100% excess pore pressure ratio) in the loose sand layer. Determine: (i) where the water levels (relative to the ground surface) would be in both piezometers if they had sufficiently tall "riser" sections – i.e., portions that extend above ground, and (ii) the average hydraulic gradient between the depths of the slotted intervals for the two piezometers.
#### Part D
For the conditions given in (c), determine the total horizontal stress at the depth of the slotted interval for Piezometer B if the value of Ko is unaffected.
### Solution:
#### Part A
Figure 2. Rough sketch of Problem 2.

\begin{tabular}{*{4}{c}} \text{Piezometer} & \text{Elevation Head [m]}, h_z & \text{Pressure Head [m]}, h_p & \text{Total Head [m]}, h_T \\ \hline \hline A & 6 & 2 & 8 \\ \hline B & 0 & 8 & 8 \\ \hline \end{tabular}

Table 2. Hydrostatic head on piezometers using bottom of piezometer B as the datum.

The water levels in the piezometers will be where the groundwater table is (i.e. z = 2 m).

i_{A\rightarrow B} = \frac{\Delta h_{T, A \rightarrow B}}{\Delta L} = \frac{8 \ m - 8 \ m}{10 \ m - 4 \ m} = 0

#### Part B
\sigma_{hB}' = K_0 \sigma_{vB}' = K_0 \left[\gamma_{clay} (3 \ m) + \gamma_{sand} (7 \ m) - \gamma_w (8 \ m)\right]

\sigma_{hB}' = 0.5 \left[18 \ \text{kNm}^{-3} (3 \ m) + 20 \ \text{kNm}^{-3} (7 \ m) - 9.81 \ \text{kNm}^{-3} (8 \ m)\right] = 57.8 \ \text{kPa}

\sigma_{hB} = \sigma_{hB}' + u_B = 57.8 \ \text{kPa} + \gamma_w (8 \ m) = 57.8 \ \text{kPa} + 9.81 \ \text{kNm}^{-3} (8 \ m)

\sigma_{hB} = 136.8 \ \text{kPa}

#### Part C
Liquefaction can only occur in the loose sand layer. When liquefaction occurs, the pressure ratio, ru, is equal to one (i.e. Δu = σv0’).

## Problem 3.
### Given:
Square footings of width B will support columns for an elevated bridge that crosses over a park that periodically floods during winter. The footings will be embedded a depth Df in a deep deposit of medium-dense gravelly sand having an effective friction angle of 35 degrees. The water level can rise to about 5 feet over the ground surface. The unit weight of the gravelly sand is about 128 pcf when saturated. The design dead plus live loads imposed on each footing are a vertical load of 320 kips (along the centerline of the footing), a horizontal load of 60 kips (at the column base), and an overturning moment of 180 kip⋅ft (in one direction only).
### Find:
Perform all calculations in SI units.
#### Part A
Determine the minimum footing width B required to provide a factor of safety against bearing failure of 3.0 for embedment depths (D) ranging from 1 to 6 feet.
#### Part B
Plot the minimum B versus D.
### Solution:
#### Part A
Constant soil parameter values of γ’ = 10.3 kNm-3, \phi' = 35 ^ \circ , and F.S. = 3 were used. Constant load values of Qv = 1423.3 kN, Qh = 266.9 kN, and ML = 244.0 kNm were used.

The eccentricity, e, was calculated as follows.
e = \frac{M_L}{Q_v} = \frac{244.0 \text{kNm}}{1423.4 \text{kN}} = 0.17 \text{m}

The following equations were used to calculate the factors in Table 2.
L_{eff} = B

B_{eff} = B - 2e = B - 2(0.17 \ \text{m}) = B - 0.34 \ \text{m}

\beta = tan^{-1} \left(\frac{Q_h}{Q_v}\right) = tan^{-1}\left(\frac{266.9 \text{kN}}{1423.4 \text{kN}}\right) = 10.6^\circ

N_q = \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} \text{exp}\left[ \pi \text{tan}\phi' \right] = \frac{1 + \text{sin}35^\circ}{1 - \text{sin}35^\circ} \text{exp}\left[ \pi \text{tan}35^\circ \right] = 33.3

i_q = \left( 1 - \frac{\beta}{90^\circ}\right)^2 = (1-\frac{10.6^\circ}{90^\circ})^2 = 0.778

N_\gamma = 1.5(N_q -1) \text{tan}\phi' = 1.5 (33.3 - 1) \text{tan} 35^\circ = 33.9

i_\gamma = \left( 1 - \frac{\beta}{\phi'}\right)^2 = (1-\frac{10.6^\circ}{35^\circ})^2 = 0.485

q_0' = \gamma ' D = 10.3 \text{kNm}^{-3} D

s_q = s_\gamma = 1 + 0.1\frac{B}{L} \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} = 1 + 0.1 \ \frac{B - 0.34 \ \text{m}}{B} \frac{1 + \text{sin}35^\circ}{1 - \text{sin}35^\circ}

d_q = d_\gamma = 1 + 0.1\frac{D}{B} \sqrt{\frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}} = 1 + 0.1 \frac{D}{B} \sqrt{\frac{1 + \text{sin}35^\circ}{1 - \text{sin}35^\circ}}

These factors are able to be used to calculate the demand, capacity, and the factor of safety relationship.
q^{net} = \frac{Q_v}{B_{eff} L_{eff} } - q_0'	Demand

q_{bL}^{net}= q_0' N_q s_q i_q d_q + \frac{1}{2} \gamma N_\gamma s_\gamma i_\gamma d_\gamma - q_0'	Capacity

\text{F.S.} = \frac{q_{bL}^{net}}{q^{net}} \Rightarrow 0 = q_{bL}^{net} - \text{F.S.} q^{net}

By setting all variables in the above equation(s) in terms of B and D, the Sympy module in Python can solve the above expression for B for each given value of D from 1 foot to 6 feet (i.e. 0.3048 m to 1.8288 m).

\begin{tabular}{*{15}{c}} D \ \text{[m]}& q_0 \ \text{[kPa]} & N_q & s_q & i_q & d_q & N_\gamma & s_\gamma & i_\gamma & d_\gamma & B \ \text{[m]} & B_{eff} \ \text{[m]}& L \ \text{[m]} & q_{bL}^{net} \ \text{[kPa]}& q^{net} \ \text{[kPa]}\\ \hline \hline 0.304800 & 3.139177 & 33.296091 & 1.330114 & 0.777931 & 1.020124 & 33.920950 & 1.330114 & 0.485225 & 1.020124 & 3.252451 & 2.909568 & 3.252451 & 441.811102 & 147.270367 \\ \hline 0.609600 & 6.278354 & 33.296091 & 1.326439 & 0.777931 & 1.044546 & 33.920950 & 1.326439 & 0.485225 & 1.044546 & 2.971724 & 2.628841 & 2.971724 & 527.756773 & 175.918924 \\ \hline 0.914400 & 9.417531 & 33.296091 & 1.322743 & 0.777931 & 1.073450 & 33.920950 & 1.322743 & 0.485225 & 1.073450 & 2.734353 & 2.391469 & 2.734353 & 624.752602 & 208.250867 \\ \hline 1.219200 & 12.556708 & 33.296091 & 1.319030 & 0.777931 & 1.107024 & 33.920950 & 1.319030 & 0.485225 & 1.107024 & 2.531242 & 2.188359 & 2.531242 & 733.204376 & 244.401459 \\ \hline 1.524000 & 15.695885 & 33.296091 & 1.315295 & 0.777931 & 1.145477 & 33.920950 & 1.315295 & 0.485225 & 1.145477 & 2.355278 & 2.012394 & 2.355278 & 853.821101 & 284.607034 \\ \hline 1.828800 & 18.835062 & 33.296091 & 1.311530 & 0.777931 & 1.189067 & 33.920950 & 1.311530 & 0.485225 & 1.189067 & 2.200999 & 1.858115 & 2.200999 & 987.598397 & 329.199466 \\ \hline \end{tabular}

Table 2. Prepared spreadsheet of values used to find B given a FS = 2.5 and a variable embedded depth of foundation.
#### Part B
Figure 2. Required foundation width to achieve a 3 factor of safety with respect to embedded depth of foundation.